# dur-Solo Type 1  |  Single-panel

| Pos............................ ........................panels Pos............................ Pos............................ ........................panels Pos............................ ........................panels Pos............................ ........................panels Pos............................ ........................panels Pos............................ .....................luminaire | Delivery and installation of dur-Solo – Type 1. The raft ceilings are attached to a special substructure [see separate position] which provides positive, stress-free retention. Opening is thus possible without using tools. [The raft ceiling can be hinged from one side.] Tolerances and quality requirements according to TAIM, DIN EN 13964 and durlum Standards. Material: Optionally galvanised steel, aluminium or stainless steel Thickness: According to strength requirements Surface finish: D206-700 white powder coated similar to RAL 9016, optional colour RAL ............... Coating thickness: Approx. 70 µm Perforations: Choice of types ............... Sound absorption: By means of a special durlum acoustic fleece s = approx. 0.73, optionally in black or white Panel: ............... Dimensions: Length ............... mm [max. 3000 mm] Width ............... mm [max. 1300 mm] €/panel Start-up costs depending on format, training and call-up € Delivery and installation of a durlum substructure consisting of two transverse members suspended from the ceiling by means of 2 x 2 threaded rods. Disengagement allows the raft ceiling to hinge. Height below structural ceiling: ............... mm It is only permissible to use structure components that have been approved by the manufacturer of the raft ceiling. All parts are of galvanised steel. €/panel Extra for tack-welded corners – recommended for hinged panels. €/panel Extra for light unit cut-outs with folded edges. €/panel Extra for reinforced mounting for pendant luminaires, e.g. Type PEGASUS. €/panel Luminaire “1430” suitable for installation in raft ceiling Type 1, including edges folded for reinforcement, BAP parabolic louvre design, with electronic ballast, ready to connect and installed in panel. Lamp options: 1 x 14 W FH/1 x 24 W FQ 1 x 21 W FH/1 x 39 W FQ 1 x 28 W FH/1 x 54 W FQ 1 x 35 W FH/1 x 80 W FQ €/luminaire |
| --- | --- |