# PYTHA® | Multidirectional louvre – mounted on T24 carrier

Double blade open cell ceiling consisting of a substructure [T-shaped rail] and prefabricated panel elements.

The T-shaped rails of 1000 mm in length are suspended rigidly from the mounting level [e.g. bare ceiling] via a suspension hanger for threaded rods with M6 threaded rods using technical approved dowels [distance of the suspensions according to EN 13964]. The distance between the T24-profiles is 1200mm.

Cross carriers T24 of 1200mm in length which are snap-fitted in the punched slots of the longitudinal profiles friction-locked at the module spacing form a carrier so that the individual panel elements can be placed on the T-profiles [visible construction].

All parts are made of pre-coated or anodized aluminium.

| Pos. m² | Panels – PYTHA® multidirectional open cell ceiling Panel size: 1200x1200mm Blade width/height: 9/40mm Step: 120mm Colour: ............... [Other colours on request] Material: Aluminium Unit price: ............… €/m² Total price: ............… € |
| --- | --- |
| Pos. m² | T-shaped rail [T24] as longitudinal profile Colour:  White Other colours on request Length: 2400mm Unit price: …............ €/m² Total price: ............… € |
| Pos. m² | T-shaped rail [T24] as cross profile Colour:  White Other colours on request Length: 1200mm Unit price: …............ €/m² Total price: ............… € |